## Slide 1: Paging
Additional slide courtesy: Prof. Mandar Mitra

## Slide 2: A relook at run-time address binding
Logical address / virtual address  Compiler generated
Physical address  What goes on the bus to address physical memory
Logical Address Space
0
1004
MAX
a.out
14K
15004
LOAD
RUN
COMPILE

## Slide 3: Runtime address binding
1004
15004
14K

## Slide 4: Context Switch
Logical Address Space
0
1004
MAX
a.out
14K
4004
PCB
For a.out process

## Slide 5: Memory Management Unit
1004
4004
3000
3K
a.out comes back

## Slide 6: Paging
Physical address space of a process can be noncontiguous; process is allocated physical memory whenever the latter is available
  Avoids external fragmentation
  Avoids problem of varying sized memory chunks
Divide physical memory into fixed-sized blocks called frames
  Size defined by hardware
  Size is power of 2, between 512 bytes and 16 Mbytes
Divide logical memory into blocks of same size called pages
Kernel to keep track of all free frames

## Slide 7: Paging
x
x
Logical Address Space (LAS)
Physical Address Space (PAS)
s
s
s
..
s
Given a logical address aL,
compute the page number as
floor (aL / s) and the offset d as aL mod s
If we take s = 2n, then we have the lower
n bits of aL selecting the offset, and the higher bits
selecting the logical page number
aL
d
d
2m

## Slide 8: Address Translation Scheme
Address generated by CPU is divided into:
  Page number (p) – used as an index into a page table which contains base address of each page in physical memory
  Page offset (d) – combined with base address to define the physical memory address that is sent to the memory unit
  For given logical address space 2m and page size 2n

## Slide 9: Paging
To run a program of size N pages, need to find N free frames and load program
Set up a page table to translate logical to physical addresses
Still have Internal fragmentation
  If things are uniformly distributed, waste about half a page per process
  For given logical address space 2m and page size 2n, 2m-n entries in PT

## Slide 10: Paging Hardware
Address translation from LAS to PAS done by MMU
Question: Page size depends on OS or hardware dependent?
Question: What all circuits for implementation?

## Slide 11: Paging
x
x
Logical Address Space
Physical Address Space
s
s
s
..
s
aL
d
d
Addr(f2)
Addr(f6)
Given a logical address aL,
compute the page number as
floor (aL / s) and the offset d as aL % s
If we take s = 2n, then we have the lower
n bits of aL selecting the offset, and the higher bits
selecting the logical page number
  Multiplexer
Also, we have all frame addresses as multiples of s (2n), so lower n bits of
Frame address are definitely 0. So addition of page number with d is simply
address concatenation  MMU is very simple.

## Slide 12: Paging Example
Logical address: n = 2 and m = 4. Using a page size of 4 bytes and a physical memory of 32 bytes (8 pages)

## Slide 13: Free Frames
Before allocation
After allocation
Implementation?
A simple bit vector?

## Slide 14: Paging

## Slide 15: Internal Fragmentation
Internal Fragmentation – allocated memory may be slightly larger than requested memory;
  Memory within a partition may be left unused

## Slide 16: Paging

## Slide 17: Implementation of Page Table

## Slide 18: Implementation of Page Table
One for the page table and one for the data / instruction

## Slide 19: Implementation of Page Table

## Slide 20: Translation Look-Aside Buffer
TLBs typically small (64 to 1,024 entries)
On a TLB miss, value is loaded into the TLB for faster access next time
  Replacement policies must be considered
Question: What kind of TLB hit ratio do you expect to get?

## Slide 21: Effective Access Time
  Hit ratio – percentage of times that a page number is found in the TLB
An 80% hit ratio means that we find the desired page number in the TLB 80% of the time.
Suppose that 10 nanoseconds to access memory.
  If we find the page in TLB then a mapped-memory access take 10 ns
  Otherwise we need two memory access so it is 20 ns
Effective Access Time (EAT): average time for memory access (including TLB lookup)
EAT = 0.80 x 10 + 0.20 x 20 = 12 nanoseconds
implying 20% slowdown in access time
Consider a more realistic hit ratio of 99%,
  EAT = 0.99 x 10 + 0.01 x 20 = 10.1ns
implying only 1% slowdown in access time.

## Slide 22: Memory Protection
Memory protection implemented by associating protection bit with each frame to indicate if read-only or read-write access is allowed
  Individual process
    Example: Jump instruction to a target address
      While I am executing an instruction, can I edit my code section during execution?
      How does the kernel enforce this?
        protection bit checked in parallel with address computation
        MMU can raise a memory
        exception when needed
  Across processes
    Automatically ensured
    Think: structure of logical
    address
Kernel
P1
P2
P1

## Slide 23: Valid / Invalid it
Question: What happens if the program generates an invalid logical address?
  Last n-bits are 0, use 3 of them to set rd / wr / x permission
  One more bit
Valid-invalid bit attached to each entry in the page table:
  “valid” indicates that the associated page is in the process’ logical address space, and is thus a legal page (did the compiler map to this page?)
  “invalid” indicates that the page is not in the process’ logical address space
Violation causes hardware trap to kernel

## Slide 24: Valid (v) or Invalid (i) Bit In A Page Table

## Slide 25: Shared Pages
Shared code
  One copy of read-only code shared among processes (i.e., text editors, compilers, window systems)
  Also useful for interprocess communication if sharing of read-write pages is allowed
Private code and data
  Each process keeps a separate copy of the code and data
  The pages for the private code and data can appear anywhere in the logical address space

## Slide 26: Shared Pages Example

## Slide 27: Structure of the Page Table
Multi-level paging I

## Slide 28: Multi-level paging II / Hierarchical PT
where p1 is an index into the outer page table, and p2 is the displacement within the page of the inner page table

## Slide 29: 2-level Page Table example
Break up the logical address space into multiple page tables
We then page the page table
Known as forward-mapped page table

## Slide 30: Address-Translation Scheme

## Slide 31: 64-bit Logical Address Space
Even two-level paging scheme not sufficient
If page size is 4 KB (212)
  Then page table has 252 entries
  If two level scheme, inner page tables could be 210 4-byte entries
  Address would look like
  Outer page table has 242 entries or 244 bytes
  One solution is to add a 2nd outer page table
  But in the following example the 2nd outer page table is still 234 bytes in size
    And possibly 4 memory access to get to one physical memory location

## Slide 32: Three-level Paging Scheme